## Slide 1
State Machine
with Debounce

## Slide 2
Design Description:
When push button is pressed to generate a single transition from 0 to 1 or from 1 to 0, it generates multiple transitions because of the tendency of any two metal contacts to bounce.
Debounce circuit aims to eliminate the multiple transitions.
When push button is pressed, it should trigger a counter and your circuit should ignore input for a short while. That is, for as long as the timer counts.

## Slide 3
Design I/O:
rst: 1 bit input for reset
clk: 1 bit input for clock
btn: 1 bit input coming from a push-button
ledOut: 3 bit output
SM
rst
clk
btn
ledOut
1
1
1
3
debounce
1
btnD
State Machine with Debounce (SMD)

## Slide 4
Design Behavior:
btn == 1
btn == 1
btn == 1
btn == 1
btn == 0
btn == 0
btn == 0
btn == 0
ledOut = 001
ledOut = 010
ledOut = 011
ledOut = 100
State machine part of your design is the same.
For debounce circuit, your design should ignore input for a short while after push button is pressed. To do that, you should trigger a counter and while counting you should ignore input.