## Slide 1
Calculator

## Slide 2
Design Description:
This design is a simple calculator capable of 6 different operations. (such as: *, +, -, x2, ++, --)
The design will take one number (from switches) at a time and validate the number by a ‘valid’ input from a push button.
Depending on the operation, the circuit will need one or two operands, which will result in either 2 or 3 states per calculation.
Led outputs should output the input number or operand until the result is calculated.

## Slide 3
Design I/O:
rst: 1 bit input for reset
clk: 1 bit input for clock
btn: 1 bit input coming from a push-button
ledOut: 3 bit output
Calculator
rst
clk
validIn
ledOut
1
1
1
8
dataIn
8

## Slide 4
Design Behavior:
(valid == 1)
ledOut = Number
(valid == 1
&&
operand == 0||1||2)
ledOut = Operand
(valid == 1)
ledOut = Result
(valid == 1
&&
operand == 3||4||5)
ledOut = Result
(valid == 0)
ledOut = Result
(valid == 0)
ledOut = Number
(valid == 0)
ledOut = Operand
The calculator to be implemented should use the state machine to the left.
At every state, whenever the situations shown in its brackets are satisfied, the circuit will go to the intended state and output the equation below brackets.